## Slide 1: Project 1: Brake System Modelling & Control

## Slide 2: Objective
To determine the transfer function of air brake system consisting of electro-pneumatic regulator (EPR).
Brake pressure model
EPR Voltage (input)
Brake chamber pressure (output)

## Slide 3: Procedure - Modelling
Check for LTI approximation
Frequency spectrum
Frequency response
System transfer function
Time response
Model parameter values

## Slide 4: Check for LTI – Spectral analysis
This method feeds a sinusoidal input voltage to the system and analyses the frequency content in the output.

## Slide 5: Check for LTI – Spectral analysis
Open the frequency data files with Matlab.
Each matrix contains Time, Voltage and Pressure data.
Time
Voltage
Pressure
Frequency
Plot input and output vs time.
plot(F_0_1(:,1),F _0_1(:,2),'b')
hold on
plot(F _0_1(:,1),F _0_1(:,3),'r')

## Slide 6
Identify the dominant frequency in each input and output pair.

## Slide 7
Make a stem plot of magnitude vs frequency for both input and output.
Example: stem(frequency,magnitude)
Check if the system can be approximated as an LTI system.
Type this in the command window and press enter to call the function.
Input arguments passed to the function
Output arguments returned from the function

## Slide 8: Frequency response –Bode plot
Get the peak to peak output values for each frequency (use min() max() command in Matlab).
Using the values obtained, calculate gain for each frequency as given below:
Plot frequency vs calculated gain using semilogx() command in Matlab.

## Slide 9: Frequency response –Bode plot
Low frequency asymptote
High frequency asymptote
Check for the slope of high frequency asymptote.
Slope (dB/decade) | Relative degree of the system
-20 | 1
-40 | 2
-60 | 3

## Slide 10: Transfer Function Structure
Using Pade’s Approximation,
Model values to be found

## Slide 11: Step Response Analysis
Import the data
Plot the step input and response
Find the delay and gain
Determine the time constant

## Slide 12: Step Response Analysis
1. Import step response data
Step response data for 5V input
Time
Voltage
Pressure

## Slide 13: Step Response Analysis
2. To plot the data for step response
Time
Voltage
Pressure
Time

## Slide 14: Step Response Analysis
3. To determine the delay and steady state gain of the system
Measure the time delay from the response plots and note down your observations.
Measure the input and output steady state values and calculate gain as the ratio of P_s/V_s which is in bar/V.
Input steady state voltage (V_s)
Output steady state pressure (P_s)

## Slide 15: Step Response Analysis
4. Determine the time constant
Determine the time constants for all the four sets and check if it is same.
If not find the range in which it lies.

## Slide 16: Time constant
With the τ range obtained from previous exercise, assume a suitable step size and obtain a set a values for the same.
  Example: If the range is [0.1 0.4] and the assumed step size is 0.05, the set will consist of {0.1,0.15,0.2,0.25, 0.3, 0.35, 0.4}.
With delay and gain value obtained, use the code given below to find the simulated response for the above set and compare it with experimental response.
Time constant values in an array
Step input magnitude
Time range for simulated response

## Slide 17: Time constant
For comparison, calculate Mean Absolute Percentage Error (MAPE) for the time constant value set obtained earlier.
N- total number of observations.

## Slide 18: Time constant
Compute MAPE for each τ value for all the voltages given and find the τ value for which it is minimum.
Hints to program in Matlab:
Use ‘for loop’ to implement the MAPE formula.
Time constant | MAPE for V1 | MAPE for V2 | MAPE for V3 | MAPE for V4 | Average MAPE
 | … | … | … | … | …
 | … | … | … | … | …
 | … | … | … | … | …
 | … | … | … | … | …

## Slide 19: Gdrive link
https://drive.google.com/file/d/1C39mDgku0anc0vufnhKzKuuYiaA24FCb/view?usp=sharing